## Slide 1: HelioCon SolTrace Tutorial Session I: A Beginner’s Overview
Allan Lewandowski
May 19, 2022

## Slide 2: Outline
Session I
  Basic operation and capabilities
  Simple examples
    Single element parabolic dish with target
    Single element heliostat
      Vector geometry overview
    Single element trough with receiver
Session II
  Questions/clarifications from Session I
  In-depth examples
    NREL HFSF
    Heliostat field with flat target
      CRTF with Excel-generated inputs
      Alternative receiver geometries

## Slide 3: SolTrace
Background
  Roots at NREL more than 30 years ago when designing HFSF
  Numerous staff contributed to development
  Evolved over the years to be very versatile
  Current version is 3.1
What is it?
  Open-source software tool using Monte Carlo ray-trace methodology
    Follows Spencer and Murty 1962 paper on tracing procedure
    Written in C++, uses wxWidgets toolkit, runs on Windows, Linux/Unix and Mac OS X operating systems
  Useful for almost all CSP concepts and many standard optical elements
  Can use multiple CPU cores/threads for very fast tracing
  Generates optical performance results at a specific moment in time
    Has a scripting capability for running multiple cases
What it doesn’t do
  Spectral calculations
  Keep track of ray power; only scaled with user DNI input

## Slide 4: SolTrace Organization
Coordinate systems
  Global, stage and element
    User selects either Earth-oriented or user-defined global coordinate system
Fundamental component is the element
  Elements are defined in stages by position and orientation within a stage
  Stages are defined relative to the global coordinate system by position and orientation
    Elements are defined relative to the stage system
  Multiple elements and stages can be set up by the user according to system geometry
  Geometry is saved as a “.stinput” file
Main window of SolTrace 3.1
  We’ll go over each of these in some detail switching to a live view of 3.1
Notes: Go over each tab with quick summary
Menu: open, close, saving files
Sun: defines global geometry and sunshape
Optics: reflective/refractive properties of surfaces
Geometry: stages and elements
Trace: initiates ray tracing
Intersections: shows ray intersections on selected elements and stages along with optional ray paths
Flux maps: 2d flux maps for flat or cylindrical surfaces
Data: options for viewing detailed ray data

## Slide 5: Sun
Point source – not normally used and has possible bug
Sun position and all further coordinate system orientations
  Where does the z-axis point
  Lat, day, hr – sets up Earth oriented system
    X is west, Y is up, Z is north
    SolTrace converts these inputs to x,y,z according to simple solar time equations
      Need to use those equations in your external calculations for accurate results
    Local time not considered
Sun shape
  Several options available
  Predefined/Load has a bug which allows only csv files to be loaded
    Numerous csr files are included in folder
      Those files can be opened externally, then copy and paste values to User Defined table

## Slide 7: Optics
Reflective or refractive element properties
Add to start entering data
Note there is both front and back side properties
  Reflectivity
  Transmissivity – only applies to refractive elements
  Slope error
  Specularity error
  Error type
    Gaussian
    Pillbox
    Diffuse
  Several not used
  Refractive elements require only real index (and transmissivity)

## Slide 9: Geometry – Stage inputs
Add stage and Insert element to bring up data entry
Stages can be Virtual (do no interact with rays, but intersection data is saved
  1st stage cannot be Virtual
Multiple hits checked if interactions between stage elements are possible
Trace through if rays might miss any element in stage but interact with downstream stages
Origin: where is stage positioned in global coordinates
Aim point: where does z-axis point in global coordinates (note not a vector)
Z-rotation: self explanatory
Various editing options: try them yourself

## Slide 11: Geometry – Element inputs
En: is this element enabled, not checked – ignored by trace
Position: relative to stage coordinate system
Aim point: relative to stage coordinate system
Z-rot: rotation of x,y axes about z-axis (clockwise if z is up)
Aperture: 8 values can be manually entered or selected with “Aperture”
  Various aperture types allowed, most require 1 or 2, some all 8 values
  All defined in element x-y plane
  See expanded Help section for further details
Surface: shape of element, typically in x-z plane
  See expanded Help section for details on usage for some surfaces
Data transfer: Import/Export not clear what this does!

## Slide 13: Trace
# ray intersections: limited only by memory
Seed: same seed will generate same set of random rays, -1 random seed each time
Include
  Sun shape: unchecked would be point source
  Optical errors: unchecked would be perfect optics
  Point-focus system: odd name, but for stages where elements will interact, checked limits tracing to nearest neighbors, really speeds up heliostat field traces
Working folder: really should be in Menus, but this saves all the data and inputs in folder of your choice
Some runtime errors are trapped if geometry cannot be resolved or input errors are detected
A note of tracing procedure
  Parallel rays are traced in first stage within extents of elements
  Sun shape and optical properties are applied at initial intersection and on reflection

## Slide 15: Intersections
Shows ray intersections and ray paths for selected stages and elements
Can select coordinate system, global is the most appropriate unless looking at specific stages/elements
Final intersection points: rays absorbed only
DNI: here is where user scales power, be consistent with units of length and flux (use metric and suggest 1kW/m2 to keep power in kW)
Plot paths: can select specific rays, is useful in some geometry diagnostics
Include missed: shows rays that don’t hit elements
Pan and zoom with typical keyboard combinations with mouse, don’t bother with axis scale factors

## Slide 17: Flux maps
Only flat or cylindrical (unwrapped) surfaces are allowed
Note on binning: data shown is cell-centered therefore does not extend out to actual edge of the element
Autoscale: checked shows maximum extents of data, unchecked – user can enter values
DNI: independent of value in Intersections (should be fixed)
Final only: absorbed rays only, otherwise incident
Several range color schemes selectable
Write data files: 2 different data formats – one easily imported into Excel (flx) and the other into Tecplot (very comprehensive data plotting package once used at NREL)

## Slide 19: Data
View export detailed ray intersection and direction data
Coordinate system and specific stages can be selected
Lists ray intersection by ray number with direction cosines of incident ray, element and stage number
Very useful for looking at both detailed ray information and for assessing other types of information (e.g., angular data distributions). Also useful for organizing and sending data to other visualization software.

## Slide 21: ? Help
Unfortunately, the Help in 3.1 takes you to a 2013 NREL report that is not very helpful as it has limited details.
Version 3.2 has a more complete Help but with some omissions and needs an update

## Slide 22: Example 1 - Generate together assuming 3.1 up and running
Single element parabolic dish
  Sun: Global coordinate system at origin and z-axis pointing up – not Earth oriented
    4.65mrad pillbox
  Optics: some set of reflective properties
  Stage 1 with 1 element as the dish
    Stage and element coordinate systems align with global
    D=5 (meters), f/D=0.6 (f=3)
  Stage 2 with 1 element as a target at focal point
    Vary target position and size

## Slide 23: Example 2
Single element heliostat
  Sun: pick latitude, day, hour
    Need to generate unit vector to sun using same equations as SolTrace
  Optics: some set of reasonable properties for a heliostat
  Stage 1 aligned coordinate systems to global, Stage 2 oriented to target
  Stage 1 with 6 elements as eSolar heliostat panel
  Stage 2 with 2 large, virtual elements placed between heliostat and tower
  Need to review vector math for heliostat pointing
    Let’s use an existing spreadsheet developed for an eSolar field built by SunDrop Fuels.
      NREL paid to have the field packed and shipped to a solar test facility near DIA (SolarTAC), originally established by Xcel Energy

## Slide 24: Vector math
Euler angles
Rotation matrix
Note that in my spreadsheets AL = -
  This is due to my assumption that the y-axis rotation follows the normal Earth angular convention (e.g., clockwise is positive, unlike (1) above)

## Slide 25: Heliostat normal vector and aim point
Note: for single element heliostat no rotation matrix need be applied as vectors can be directly calculated from position of sun, heliostat and target
  Calculate heliostat-sun unit vector
  Calculate heliostat-target (or aim point) unit vector
  Calculate nominal aim point vector (bisecting vector)
  Add any pointing error
  Calculate new aim point vector and extend to aim point
For multi-element heliostat, facet canting is first applied in the heliostat coordinate system (x-y plane is horizontal-vertical; z pointing north)
  Calculate canting angles, normal vectors and any errors
  Apply rotation matrix with =clockwise rotation (AL convention), =elevation angle, =0 (no z-rotation)
    Have not yet figured out why heliostat samples have ≠0
  Calculate new rotated position, aim point vector and extend to aim point