## Slide 1: HelioCon SolTrace Tutorial Session II: Implementing Advanced Geometries
Allan Lewandowski
May 20, 2022

## Slide 2: Outline
Session I review
  Went over basic operation and several examples
  Any burning questions?
Today’s outline
  More complex examples (meaning more work outside SolTrace)
  NREL’s High Flux Solar Furnace (HFSF)
    Slightly different arrangement of coordinate systems
    Options for plate and ‘Venetian blind’ attenuators
    Simple target plane at focus
  CRTF heliostat field (canted heliostat panels)
    Requires rotation of panels after canting in heliostat plane
  Questions
  Who to contact in the future

## Slide 3: HFSF Coordinate Systems
Note stage 2 coordinate system and global system are aligned
  This made it somewhat easier to define the primary reflector array
Stage 1 is the heliostat and defined relative to global system with surveyed data for drive pivot point
Stage 3 is the target located at the nominal focal point of and pointed at center of primary array

## Slide 4: HFSF Spreadsheet
Older, not as well organized but still functional
  Includes options for plate or blind attenuators
  One stinput has secondary input option where SolTrace does not appear to open the cubic spline data file, not sure why
  Look at difference between runs with pillbox sun and CSR40 sun (low DNI value compounds peak flux reduction)

## Slide 5: Heliostat normal vector and aim point
Note: for single element heliostat no rotation matrix need be applied as vectors can be directly calculated from position of sun, heliostat and target
  Calculate heliostat-sun unit vector
  Calculate heliostat-target (or aim point) unit vector
  Calculate nominal aim point vector (bisecting vector)
  Add any pointing error
  Calculate new aim point vector and extend to aim point
For multi-element heliostat, facet canting is first applied in the heliostat coordinate system (x-y plane is horizontal-vertical; z pointing north)
  Calculate canting angles, normal vectors and any errors
  Apply rotation matrix with =clockwise rotation (AL convention), =elevation angle, =0 (no z-rotation)
    Have not yet figured out why heliostat samples have ≠0
  Calculate new rotated position, aim point vector and extend to aim point

## Slide 6: Vector math
Euler angles
Rotation matrix
Note that in my spreadsheets AL = -
  This is due to my assumption that the y-axis rotation follows the normal Earth angular convention (e.g., clockwise is positive, unlike (1) above)

## Slide 7: CRTF Spreadsheet
More recent, pretty comprehensive spreadsheet done with Univ Colorado in attempt to match SolTrace model with power and flux data from NSTTF
  Model has ability to set multiple focal length and canting schemes within the field
    On-axis canting assumed but schemes can include several options
    Includes multiple error options for canting, tracking and focal length